# Tree Protection in the 
City of Melbourne

### Information for planners, developers, service providers and contractors

The protection of trees is vital to retaining our city’s character and environment. Trees grow in a delicate balance with their environment and any changes to that balance must be minimized if the tree is to remain healthy state and fulfil its potential. It is rarely possible to repair stressed and injured trees, so damage needs to be avoided during all stages of development and construction.

This document guides work around trees to ensure their long-term protection, integrity and vitality and applies to all trees in the municipality that are either owned or managed by the City of Melbourne.

In all cases, Melbourne City Council’s arborists shall, within the parameters of best practice and meeting the community’s expectations, have the discretion to modify or add to any condition, practice or standard outlined within the policy. All construction and development works near public trees must abide by the protection and retention requirements outlined in this document.

### Tree Protection Requirements

The most important consideration for the successful retention of trees is to allow appropriate above and below ground space for the trees to continue to grow. This requires the allocation of Tree Protection Zones for retained trees. A protection zone should be established for the duration of the project. Care must be taken to ensure that no damage is caused to council tree trunks, roots, canopy or branches during construction.

##### To ensure that public trees in the municipality are fully protected at all times, the following requirements must be complied with:

### a - Tree Protection Zones

- A Tree Protection Zone (TPZ) shall be established for the duration of any works near a tree.

- The tree protection distance method outlined in the current Australian Standard will be used for the allocation of tree protection zones. The TPZ for individual trees is calculated based on trunk (stem) diameter (DBH), measured at 1.4 metres up from ground level. The radius of the TPZ is calculated by multiplying the tree’s DBH by 12.  For example; a tree with 40cm DBH requires a TPZ of 4.8 metres. The method provides a TPZ that addresses both tree stability and growth requirements. TPZ distances are measured as a radius from the centre of the trunk at ground level.

- The Council’s arborist must approve any modification to a tree protection zone

| Trunk Diameter (DBH) | Tree Protection Zone (TPZ) |
| --- | --- |
| 10cm | 1.2m |
| 20cm | 2.4m |
| 40cm | 4.8m |
| 75cm | 9m |
| 100cm | 12m |

Table 1: Example Tree Protection Zone

##### The following are not permitted within a tree protection zone:

- Mechanical excavation on the road, footpath or any public space

- Stockpiling of building materials, debris or soil

- Vehicular traffic except on existing paved surfaces

- Installation of service pits or hatches

- Vehicular crossings

- Severing of tree roots with a diameter greater than 30mm

- Alteration of soil levels and structure

### B – Boring

- Installation of underground services are to be bored

- Entry and exit pits will be positioned outside the designated TPZ of each tree. This requirement should apply unless root sympathetic exploratory investigations have been undertaken and it has been determined that access within the TPZ will not significantly affect the tree.

- The extent or length of boring in the vicinity of trees will be determined by the TPZ.

- The depth of the boring will depend on the size of the tree. Table 2 indicates the recommended boring depths for trees based on their trunk diameter.

- Where boring is unavailable, excavation shall be by hand or non-destructive digging.

| Trunk diameter | Minimum Depth to TOP |
| --- | --- |
| <100cm | 800mm |
| 100-150cm | 950mm |
| >150cm | 1100mm |

Table 2: Depth of boring

### Pruning

- No council tree may be pruned or branches removed by anyone other than those authorised by council

- Pruning of roots and branches will be in accordance with AS 4373, Pruning of Amenity Trees or any more recent relevant Standard.

### Removal

- Removals of trees will not occur unless approved by the Council.

- No council tree may be removed by anyone other than those authorised by the Council.

- Where a public tree removal is approved by the Council’s arborist in relation to a development, the associated cost of the tree and its removal shall be paid by the property owner or a representative prior to the removal.

### Hoarding and Gantry

- Where a gantry or hoarding is to be constructed over a footpath the placement of the footings and gantry structure must not adversely impact trees. Structures must be placed more than 0.5m away from tree trunks, branches or roots.

- If a tree is enclosed within the hoarding or gantry space, the owner and/or builder are responsible for implementing a maintenance program for affected trees as approved by the Council.

### Tree Protection Management Plans

- Permission from the Council’s arborist is required for activities that do not comply with the above measures.

- A Tree Protection Management Plan endorsed by the Council’s arborist will be prepared prior to the commencement of the works.

- A Tree Protection Management Plan is developed in accordance with the Australian Standard AS 4970-2009 Protection of trees on development sites or any more recent standard. It is prepared by a certified arborist to assess impacts to public trees, provide recommendations to reduce impacts on public trees and identify construction guidelines to be followed through all phases of construction.

### Tree Protection Bonds

Where construction activities have the potential to impact public trees, a bond for the protection of the tree will be held by the Council. The amount of the bond will amount to the combined tree amenity and ecological value and will be held for the duration of the works, subject to an approved Tree Protection Management Plan.

For further information please contact the City of Melbourne on 03 9658 9658 
or email: trees@melbourne.vic.gov.au